a)

Scale factor for the basis of 20 moles of Toluene and 100 moles of Hydrogen mixture:
1.42358

For this part, assuming 100% recovery of Benzene the stream coming out of Requil is assumed to have flow rate of 265 mol / s

Work required for compressing the hydrogen feed stream=41192.3814	kW(from the results table of the reactor)

Energy required to heat the hydrogen stream fed to reactor = -3596.30830 kW(from the results table of the reactor)

Energy required to heat the toluene stream fed to reactor = 61406.53495 kW

Total energy removed or added to the two reactors to maintain isothermal conditions = -13697.64989 -129.97839 = -13697.64989 + 129.97839 = -13567.6715 kW

b)

  i)	Composition of the vapour stream from the second flash(BENZENE stream):

	TOLUENE	HYDROGEN	METHANE	BENZENE	DIPHENYL
MOLE FRACTION	0.22079	0.00973505	0.019816	0.74960	6.5369E-05

  ii)	Composition of the vapour stream from the first flash(FLASHV stream) :

	TOLUENE	HYDROGEN	METHANE	BENZENE	DIPHENYL
MOLE FRACTION	0.0004954	0.793719	0.201334	0.0044516	7.48506E-09

  iii)	Total Flow rate of recycle 1 = 33379.73076 mol/s

	TOLUENE	HYDROGEN	METHANE	BENZENE	DIPHENYL
MOLAR FLOW RATE / (mol/s)	16.53644	26494.14209	6720.46008	148.59189	0.000249850

  iv)	Total Flow rate of recycle 2=51.31497 mol/s

	TOLUENE	HYDROGEN	METHANE	BENZENE	DIPHENYL
MOLAR FLOW RATE / (mol/s)	21.486044	0.000225220	0.0022834	29.028126	0.798292

    v)	Amount of energy added/removed to the flash units:

Flash 1:	-814790.2046796 kW

Flash 2:	13844.557753308001 kW

Totally 8000945.6469 kW is removed from the flash units.

   vi) Toluene fresh-feed flow rate = 351.787 mol/sec

c) To improve the yield of Benzene- if Hydrogen is present in excess it promotes the backward reaction in the diphenyl formation reaction (2Benzene <=> Diphenyl + H2) and reduces formation of diphenyl.