Assignment 2
1)a)

So for given composition of streams the final mixed stream should correspond to the following mole fractions:
0.5 MIBK
0.45 H2O
0.05 Acetone

This corresponds to the third tie line.

Therefore from the results table,
1. Concentration of Acetone in Extract Phase(MIBK) = 0.0756339
2. Concentration of Acetone in Raffinate(water as solvent) = 0.0135143

b)

Stream	Flow Rate(kmol/hr)	Mole Fraction of Acetone	Mole Fraction of MIBK	Mole Fraction of Water
Extract	122.252832	0.0734646	0.815580	0.110956
Raffinate	77.747168	0.0131033	0.983127	0.00376985

Fraction of extracted Acetone = (Moles of Acetone in Extract)/(Total moles of Acetone)
        =(8.9812)/10 = 0.89812= 89.81%
c) Fraction of extracted Acetone = (Sum of moles of Acetone in the Extracts)/(Total moles of Acetone)
        = (8.06234129243946+6.02573533306934)/10
        = 0.96393 = 96.393%

Stream	Total Flow rate(kmol/hr)	Acetone		Water		MIBK
		Flow rate(kmol/hr)	Fraction	Flow rate(kmol/hr)	Fraction	Flow rate(kmol/hr)	Fraction
Extract - 1	65.503	8.0623	0.1231	7.7854	0.1188	49.6555	0.75806
Raffinate -1	84.497	1.9377	0.02293	82.2145	0.9730	0.3445	0.0040769
Extract - 2	57.677	1.5769	0.02734	6.0257	0.1045	50.0741	0.8682
Raffinate - 2	76.820	0.361	0.00470	76.1888	0.9918	0.27044	0.00352

d) From the percentage extraction we can clearly see that TWO STAGE CROSS CURRENT EXTRACTION PROCESS IS MORE EFFICIENT because more Acetone is separated in it( greater percentage extraction).
Reasons for improved efficiency:
- Raffinate stream which still contains acetone is reused in one more extraction process using a pure solvent.
- Given that a constant fraction of the solute is extracted each time we add the same amount of solvent, if we add an infinitesimal amount of the solvent each time and the number of stages goes to infinity, we get a theoretical 100% extraction. Because even if the amount extracted each time is small, since the number of extractions is high we can completely extract it.
- So practically as we increase the number of stages we get a better percentage extraction.

2) Reaction Equation: N2+3H2 --> 2 NH3

Conditions : 500C, 150 atm

INPUT MOLE FRACTIONS			OUTPUT MOLE FRACTIONS
N2	H2	NH3	N2	H2	NH3
0.5	0.5	0	0.4999	0.3904	0.1096

Equilibrium conversion = (Ammonia formed)/(Max number of moles of Ammonia that can form by stoichiometry)
        = 0.2964 = 29.64%

Similarly for each case using the molar flow rate we can evaluate the conversion.

 a)
P is maintained constant at 150 atm.
TEMPERATURE(Celsius)	Extent of Reaction	Conversion of N2
400	0.5588	0.1863
450	0.4159	0.1386
500	0.2964	0.09880
550	0.2072	0.06907
600	0.1447	0.04823

As we increase Temperature, Conversion decreases. This is in accordance with the Le Chatelier’s principle – since this reaction is EXOTHERMIC, increase in temperature will reduce the amount of product formed. This means that conversion of Nitrogen decreases as shown by the data.
b) T is maintained constant at 500 degree Celsius
PRESSURE(atm)	Extent of Reaction	Conversion of N2
50	0.1272	0.04240
100	0.2219	0.07397
150	0.2964	0.09880
200	0.3574	0.1191

NUMBER OF MOLES OF GASEOUS REACTANTS IS MORE THAN THAT OF NUMBER OF MOLES GASEOUS PRODUCTS per mole of the reaction, so when the system volume is less product formation is favoured. This implies that HIGHER PRESSURE favours PRODUCT FORMATION in accordance with Le Chatelier’s principle. This implies that the conversion of Nitrogen increases as expected from the data.

3)

a) ISOTHERMAL FLASH:
Feed at 30 C and 1 atm.
Flash drum operating at 61 C and 1 atm.
Vapour and Liquid streams at 61 C and 1 atm.

	COMPOSITION OF LIQUID PHASE
MOLE / FRACTIONS	n-Hexane	ethanol	methyl-cyclopentane	Benzene
	0.12969	0.60723	0.12372	0.13936

	COMPOSITION OF VAPOUR PHASE
MOLE / FRACTIONS	n-Hexane	ethanol	methyl-cyclopentane	Benzene
	0.26004	0.38271	0.20636	0.15089

Vapour Fraction = (number of moles of vapour)/(total number of moles)
        = 0.922978
Since this is a constant pressure process, Energy change = Enthalpy change
	FEED	LIQUID	VAPOUR
Molar Enthalpy / (kJ/mol)	-179.3070	-198.3955	-139.2686
No. of Moles	1	0.07702	0.9229

so energy change = 35495.58765 kJ/kmol

b)ADIABATIC FLASH:

1. Feed at 100 C and 30 atm expanded through an isenthalpic valve to 1 atm pressure.
2. Flash drum operating at Duty = 0 J/sand 1 atm(Temperature, Pressure obtained after isenthalpic expansion).
3. Both the vapour and liquid streams are at 60.0423 C and 1 atm.

	COMPOSITION OF LIQUID PHASE
MOLE / FRACTIONS	n-Hexane	ethanol	methyl-cyclopentane	Benzene
	0.234621	0.415359	0.194492	0.155527

	COMPOSITION OF VAPOUR PHASE
MOLE / FRACTIONS	n-Hexane	ethanol	methyl-cyclopentane	Benzene
	0.302913	0.347156	0.218948	0.130983

Vapour Fraction = (number of moles of vapour)/(total number of moles)
        = 0.2252080= 22.52%